## Slide 1
Gravitational Forces | Preferably COL Models
Geopotential | Static gravity field model is based on EIGEN-GRGS.RL02, tide-free, complete to degree and order 2 up to 160 ftp://hpiers.obspm.fr/iers/eop/grgs/Models/Gravity_Field/
Third-body | JPL DE405
Solid Earth Tides | IERS 2010 standards
Ocean Tides | FES 2004 ftp://hpiers.obspm.fr/iers/eop/grgs/Models/Ocean_Tide_Loading/
Atmospheric Tides | Ray & Ponte 2003 ftp://hpiers.obspm.fr/iers/eop/grgs/Models/Atmospheric_Tide/
Atmospheric Gravity | none (integrated into the geopotential)
Earth Pole Tides | IERS2010 standards
Ocean Pole Tides | Desai 2002 up to degree 12
Non tidal oceanic gravity | none (integrated into the geopotential)
Non Gravitational Forces | Preferably COL Models
Atmospheric Drag | JB2008
Solar Radiation Pressure | applied
Albedo + Infra-Red | applied
Satellite Emissivity | none
Atmospheric density | DTM 94, with best available solar activity
Relativity | Schwarzschild model + Lense-Thirring + geodetic precession
Geometry | Preferably COL Models
Earth Reference System | ITRF 2008
Celstial Reference System | J2000, ICRF2
Pole & UT1 | The EOPC04 initial values interpolated (Lagrange polynomial method) with time intervals of 3Hr are generated by EOP Center
Precession – Nutation | IAU2000A - IAU2006, A-priori set to zero
Tidal Atmospheric Loading | none
Non tidal Atmospheric Loading | none
Solid Earth Tidal Displacement | IERS 2010 standards
Ocean Loading | Ocean tide loading models per stations are obtained from Scherneck's ocean loading site and provided in the BLQ format according to the IERS Conventions 2010
Atmospheric Loading | Not applied
Pole Tides Displacement | Solid Earth Pole tide from IERS2010
Tropospheric Corrections | GPT/GMF for radioelectrical waves and Mendes-Pavlis for SLR. One zenith delay/2hr or pass + one daily tropospheric gradient per station in North & East directions
Ionospheric Corrections | none
Satellite Antenna | 
Ground Antenna | 
Elevation angle cutoff |